## Slide 1: LED-DL Device Roadmaps
Jul. 2025

## Slide 2: Table of Contents
1
2
3
4
5
6
Local Dimming Backlight Driver
Global Dimming Backlight Driver
LCD Bias
Mini-Micro LED Driver
Illumination LED Driver
RGB LED Driver

## Slide 3: Local Dimming Automotive Backlight
Jojo
TLC6962x/3x – Q1
48/24/8 CS (100/60mA, 16V)
Ultra low headroom voltage
16-bit PWM Resolution
7-bit Dot Correction
AHVC*
Insta-Boost*
LOD/LSD/TSD/Pin diagnostic
CRC/Communication loss
Mista
TLC6964x - Q1
48 CS (100mA, 16V) x 4/8
Internal 50mΩ scan FET
Ultra low headroom voltage
16-bit PWM Resolution
7-bit Dot Correction
AHVC*
Insta-Boost*
Intelligent De-ghosting+
LOD/LSD/TSD/ Pin diagnostic
CRC/Communication loss
Stacked mode (Patented)
FuSa
Released
Development
Definition
Zeppelin
TLC69699 - Q1
Connectivity
Augmented
TLC696x2 - Q1
16 CS (30mA/60mA, 20V/50V)
15-bit PWM Resolution
AHVC*
Intelligent De-ghosting
LOD/LSD/TSD
TLC696x4 - Q1
TLC696x8 - Q1
TLC696x0 - Q1
TLC696x1 - Q1
AHVC*: Adaptive Headroom Voltage Control
TLC6C5724 - Q1
24 CS (50mA, 8V)
12-bit PWM Resolution
7-bit Dot Correction
LOD/LSD/TSD
SPI
HTSSOP
Direct drive
TLC6C5748 - Q1
48 CS (32mA, 11V)
16-bit PWM Resolution
7-bit Dot Correction
LOD/LSD/TSD
SPI
HTSSOP
Direct drive
CCSI
HTSSOP / QFN
Direct drive
CCSI
HTSSOP / QFN
Time-multiplexing
Up to 2 scans
Up to 4 scans
Up to 8 scans
FET controller
SPI / CSI
HTSSOP / QFN
FuSa
FuSa
Direct drive
Time-multiplexing
SPI-CSI* protocol conversion
UART-CSI* protocol conversion
Dimming Zone Fault Summary
SPI-CCSI* protocol conversion
CRC & Missing Clock Check
Zeppelin+
TLP69697/8 - Q1
SOT / WSON
FuSa
SOT
SPI / CSI
HTSSOP / QFN
Insta-Boost*: Boost mode optimization
Dec’25
CCSI*: Continuous Clock Serial Interface
CSI*: Cascaded Serial Interface
Sampling
Dec’26
Dec’25
Sample Time
RTM time

## Slide 4: Jojo Family | Local Dimming LED Driver
FuSa Augmented (ISO26262, ASIL-B)
FuSa Compliant (ISO26262, ASIL-B)
FuSa Capable
LED: LOD | LSD | Health check
Channel: APS | Health check
Device: UVLO | TSD | ISET out of range
Communication: CRC
Fail-safe Mode | OTP CRC | Memory CRC
Oscillator Watchdog | Communication watchdog
Programmable Safety Zone | Automatic Faults Summarizing
LED Drivers Cascaded Daisy Chain Connection
Part Number | TLC69639-Q1 TLC69629-Q1 TLC69638-Q1 TLC69628-Q1 TLC69637-Q1 TLC69627-Q1 | TLC69636-Q1 TLC69626-Q1 TLC69635-Q1 TLC69625-Q1 TLC69634-Q1 TLC69624-Q1 | TLC69633-Q1 TLC69623-Q1 TLC69632-Q1 TLC69622-Q1 TLC69631-Q1 TLC69621-Q1
Channel | 48-CH, 100mA / 60mA | 24-CH, 100mA / 60mA | 8-CH, 100mA / 60mA
Package | 1. HTSSOP-56 -Thermal PAD options: Bottom / Top 2. QFN-56 -W*L*H: 8*8*1 mm | 1. HTSSOP-32 2. QFN-32 -W*L*H: 4*4*0.8 mm | 1. SOT-16 2. QFN-16 -W*L*H: 2.5*2.5*0.4 mm

## Slide 5: Mista Family | Local Dimming LED Driver
Part Number | TLC69649-Q1 TLC69649S-Q1 TLC69648-Q1 TLC69648S-Q1 TLC69647-Q1 TLC69647S-Q1 | TLC69646-Q1 TLC69646S-Q1 TLC69645-Q1 TLC69645S-Q1 TLC69644-Q1 TLC69644S-Q1
Channel | 4 × 48-CH, 8 × 48-CH (Stacked mode) | 4 × 24-CH, 8 × 24-CH (Stacked mode)
Package | 1. HTSSOP-64 -Thermal PAD options: Bottom / Top 2. QFN-64 -W*L*H: 8*8*1 mm | 1. HTSSOP-40 2. QFN-40 -W*L*H: 4*4*0.8 mm
FuSa Augmented (ISO26262, ASIL-B)
FuSa Compliant (ISO26262, ASIL-B)
FuSa Capable
LED: LOD | LSD | Health check
Scan FET: STG | STP
Channel: APS | Health check
Device: UVLO | TSD | ISET out of range
Communication: CRC
Fail-safe Mode | OTP CRC | Memory CRC
Oscillator Watchdog | Communication watchdog
Programmable Safety Zone | Automatic Faults Summarizing
LED Drivers Cascaded Daisy Chain Connection

## Slide 6
Zone num.
Channel
Resolution
Package
Function
TLC696x1-Q1
TLC69601-Q1
TLC69611-Q1
TLC69651-Q1
TLC69661-Q1
16 Dimming zones (16 CH Direct)
30mA / 20V
Up to 15-bit PWM / Hybrid Dimming
60mA / 20V
20MHz CCSI
LED open / short
30mA / 50V
60mA / 50V
HTSSOP
Adaptive FB
QFN
Scan MOSFET controller
30mA / 20V
Up to 8 scan line
60mA / 20V
20MHz CCSI
MOSFET control
30mA / 50V
60mA / 50V
HTSSOP
De-ghosting
QFN
32 / 64 / 128 Dimming zones (2/4/8 Time-multiplexing)
30mA / 20V
Up to 15-bit PWM / Hybrid Dimming
60mA / 20V
20MHz CCSI
LED open / short
30mA / 50V
60mA / 50V
HTSSOP
Adaptive FB
QFN
TLC696x0-Q1
TLC69600-Q1
TLC69610-Q1
TLC69650-Q1
TLC69660-Q1
TLC696x2/4/8-Q1
TLC69602/4/8-Q1
TLC69612/4/8-Q1
TLC69652/4/8-Q1
TLC69662/4/8-Q1
Linglong Family | Local Dimming LED Driver

## Slide 7: TLC696x1-Q1 16 CH Direct Local Dimming Driver
Notebook / Tablet Local Dimming LED Driver
Monitor Local Dimming LED Driver
Automotive Local Dimming LED Driver
Two-wire design enables easy PCB routing and better EMC
Adaptive headroom voltage enable high system efficiency
High resolution supports high dynamic range
High PWM frequency allows high refresh rate
Applications
Features
Benefits
Power Supply Vcc Voltage Range: 3V to 5.5V
20MHz Two-Wire Interface:
  4K zone supported in 240Hz frame rate
  1.8V/3.3V bus voltage compatible
  Up to 20KHz dimming frequency
Flexible Dimming:
  Up to 15-bit brightness resolution
  Support 8-step option hybrid dimming
Current Sink:
  Max. 30mA / 60mA OUT pin current in 8-bit options
  Up to 20V / 50V OUT pin voltage
  2% (typ) channel mismatch, 2% (typ) device mismatch
Digital:
  Independent update for zero frame latency
  Support Variable Refresh Rate (VRR)
No external Components needed
Adaptive FB directly controls DC/DC
Support LED open / short protection
WCSP (2.4 mm * 1.6 mm , 0.4 mm pitch)
QFN-24 (4 mm * 4 mm, 0.5 mm pitch) for AUTO
HVSSOP-24 (6 mm * 6.1 mm, 0.5 mm pitch) for AUTO

## Slide 8: TLC696x2/4/8-Q1 Time-multiplexing Local Dimming Driver
Notebook / Tablet Local Dimming LED Driver
Monitor Local Dimming LED Driver
Automotive Local Dimming LED Driver
Two-wire design enables easy PCB routing and better EMC
Adaptive headroom voltage enable high system efficiency
High resolution supports high dynamic range
High PWM frequency allows high refresh rate
Applications
Features
Benefits
Power Supply Vcc Voltage Range: 3V to 5.5V
20MHz Two-Wire Interface:
  4K zone supported in 240Hz frame rate
  1.8V/3.3V bus voltage compatible
  Up to 20KHz dimming frequency
Flexible Dimming:
  Up to 15-bit brightness resolution
  Support 8-step option hybrid dimming
Current Sink:
  Max. 30mA / 60mA OUT pin current in 8-bit options
  Up to 20V / 50V OUT pin voltage
  2% (typ) channel mismatch, 2% (typ) device mismatch
Digital:
  Support 32/64/128 dimming zones
  Independent update for zero frame latency
  Support Variable Refresh Rate (VRR)
No external Components needed
Adaptive FB directly controls DC/DC
Support LED open / short protection
WCSP (2.4 mm * 1.6 mm , 0.4 mm pitch)
QFN-24 (4 mm * 4 mm, 0.5 mm pitch) for AUTO
HVSSOP-24 (6 mm * 6.1 mm, 0.5 mm pitch) for AUTO

## Slide 9: TLC696x0-Q1 Scan MOSFET Controller
Scan MOSFET controller for TLC696x2/4/8
One-bus design enables easy system routing
Flexible placed in serial devices
Flexible with scanning MOSTFET
Applications
Features
Benefits
Power Supply Vcc Voltage Range: 3V to 5.5V
Support up to 8 Ext. scan MOSFET supported
20MHz Two-Wire Interface:
  1.8V/3.3V Bus Voltage Compatible
Compatible with TLC696x2/4/8
Programable 6-bit line switch time
Max. 30mA / 60mA driving current
Up to 20V / 50V OUT pin voltage
Programable 7-bit individual MOSFET driving ability
Integrated upside de-ghosting
WCSP (2.4 mm * 1.6 mm , 0.4 mm pitch)
QFN-24 (4 mm * 4 mm, 0.5 mm pitch) for AUTO
HVSSOP-24 (6 mm * 6.1 mm, 0.5 mm pitch) for AUTO

## Slide 10: TLC69699-Q1 Augmented Connectivity for TLC696xx-Q1
Developed according ISO26262
  Documentation available to aid ISO 26262 system design up to ASIL B
Input voltage range: 2.5V to 5.5V
Diagnostics
  SPI CRC error detection
  SPI time out detection
  CCSI brightness and register data CRC detection
  Missing continuous clock detection
  Oscillator fault detection
  OTP CRC error detection
  Fault pin report
Low EMI
  Programmable output clock frequency
  Programmable jitter on output clock
Data ready interrupt
Operating ambient temperature (-40°C to 125°C)
Package:
  WSON-12 Wettable (3mm*3mm*0.8mm)
  SOT-14 (4.2mm*2mm*1.1mm)
Features
Benefits
Compatible with SPI controller
Missing continuous clock detection
Brightness and register data integrity inspection
Known safe state for LED drivers when SPI communication is lost
Spread spectrum continuous clock for low EMI
SPI compatible connectivity for TLC696x0/1/2/4/8-Q1
Applications

## Slide 11: TLC6C5748-Q1
Automotive Local Dimming Backlight
Automotive Pixel Lamp
Automotive RGB display
Best to drive 48 LED zones with uniformity
Perfect solution for chip-on-LED-board architecture
Direct daisy chain interface with TCON controller
Max 3 single-junction LEDs/ 1 dual-junction LED in series
Reduces system power consumption
Reduces system cost
Unlimited device cascading
Applications
Features
Benefits
AEC-Q100 Qualified for Automotive Applications (Grade 1: TA -40C to +125C)
48 Channel Outputs
  Constant Current up to 31.9mA
  Breakdown Voltage up to 11V
Constant Current and Dimming
  3-bit Max Current
  7-bit, Dot Correction for Each Channel
  Configurable Grayscale Mode: 16-bit
Precise Constant Current Regulation
  Channel-to-Channel: ± 2% (typ)
  Device-to-Device: ± 2% (typ)
Diagnostic & Protection
  LED Open/Short Detection
  Output Short to GND Detection
  Over Temperature Detection
  Thermal Shutdown
Serial Data Interface
HTSSOP-56 Package (DCA) 6.1mm x 14mm

## Slide 12: TLC6C5724-Q1
Automotive Cluster Indicators
Automotive HVAC Panel Backlighting
Automotive Local Dimming Display
Automotive Ambient Lighting
Applications
Features
Benefits
AEC-Q100 Qualified for Automotive Applications (Grade 1: TA -40C to +125C)
24 Channel Outputs
  Constant Current up to 50mA, Set via External Resistor
  Breakdown Voltage up to 8V
Constant Current
  7-bit, 128-step Dot Correction for Each Channel
  8-bit, 256-step Brightness Control for Each Color Group
PWM Dimming
  Configurable Grayscale Mode: 12-bit, 10-bit, 8-bit
Diagnostic & Protection
  LED Open/Short Detection
  Output Short to GND Detection
  Adjacent-Pin Short Detection
  Pre-Thermal Warning, Thermal Shutdown
  IREF Resistor Open and Short Detection and Protection
  GCLK Error Detection
  LOD_LSD Circuit Self Test
Serial Data Interface
Programmable Output Slew Rate
Output Channel Group Delay
HTSSOP-38 Package (DAP) 8.1mm x 12.5mm
Constant current provide good LED brightness uniformity
Full LED diagnostics features improves system reliability and safety
Individual PWM dimming and DOT correction benefits RGB LED color mixing
Programmable slew rate control optimizes the system EMI performance
Output group delay reduce the peak load of front power stage

## Slide 13: Global Dimming Automotive Backlight
1A
0.8A
0.6A
Controller
Converter
LP8866(S)-Q1
3V to 48V VIN
6 ch x 200mA (S: 150mA) ILED
Dimming Ratio 32,000:1
Power Line PFET Driver
Full Diagnostics
LP8864(S)-Q1
3V to 48V VIN
4 ch x 200mA (S: 150mA) ILED
Dimming Ratio 32,000:1
Power Line PFET Driver
Full Diagnostics
LP8876/7-Q1
4.5V to 36V VIN
4 / 6 ch x 150mA ILED, 4.5A ISW
Dimming Ratio 25,000:1
Power Line NFET Driver
Full Diagnostics
I 2C
LP8865(C)/8-Q1
4.5V to 65V VIN
1 ch x 4 / 2A ISW
Dimming Ratio >32,000:1
Multi-topology
Power
LP8867(C)/9(C)-Q1
4.5V to 40V VIN
4 / 3 ch x 120mA ILED, 3.3A ISW
Dimming Ratio 10,000:1
Power Line PFET Driver
Current Foldback w/ Ext. NTC
Stand Alone
Stand Alone
3V to 48V VIN
6 /4 ch x 150mA ILED, 5.4A ISW
Dimming Ratio 65,000:1
Power Line NFET Driver
Full Diagnostics
LP8874/5-Q1
Stand Alone
LP8870/1/2/3-Q1
I 2C
HTSSOP/QFN
Dual Phase Operation
LP8890/1/6/7-Q1
3V to 48V VIN
6/4 ch x 150/200mA ILED, 7.5A ISW
Dimming Ratio 65,000:1
Power Line NFET Driver
Full Diagnostics
LP8894/5-Q1
I 2C
HTSSOP/QFN
I 2C
HTSSOP/QFN
HTSSOP
I 2C
Stand Alone
HTSSOP/QFN
VSON
QFN
Released
Development
Definition
Sampling
HTSSOP/QFN
HTSSOP/QFN

## Slide 14: Camaro Family Overview
LP887x(D)-Q1 Isw = 5.4A
LP889x(D)-Q1 Isw = 7.5A
Single Phase
Single Phase
Dual Phase
20W
Converter
Diagnostics & Protections
NMOS Power line FET
I2C with CRC
Dual Phase Operation
$0.4 BOM cost saving
40% smaller, 70% thinner
EMI compliant without CMC
Stackable for 8-12CH display
Single
Phase
Dual
Phase
Up to 65,000:1 with PWM dimming
Up to 520,000:1 with hybrid dimming
Dimming Ratio
Dual Phase
150 mA/CH
LP8870/2-Q1 >> I2C, 6-CH
LP8871/3-Q1 >> I2C, 4-CH
LP8874-Q1 >> Standalone, 6-CH
LP8875-Q1 >> Standalone, 4-CH
150 mA/CH
LP8890-Q1 >> I2C, 6-CH
LP8891-Q1 >> I2C, 4-CH
LP8894-Q1 >> Standalone, 6-CH
LP8895-Q1 >> Standalone, 4-CH
200 mA/CH
LP8896-Q1 >> I2C, 6-CH
LP8897-Q1 >> I2C, 4-CH
Performance
Leader
150 mA/CH
LP8870D-Q1 >> I2C, 6-CH
LP8871D-Q1 >> I2C, 4-CH
LP8874D-Q1 >> Standalone, 6-CH
LP8875D-Q1 >> Standalone, 4-CH
150 mA/CH
LP8890D-Q1 >> I2C, 6-CH
LP8891D-Q1 >> I2C, 4-CH
LP8894D-Q1 >> Standalone, 6-CH
LP8895D-Q1 >> Standalone, 4-CH
200 mA/CH
LP8896D-Q1 >> I2C, 6-CH
LP8897D-Q1 >> I2C, 4-CH
Package Availability
HotRod QFN-24
4 x 4 mm
θJA = 27.6 °C/W
HTSSOP-28
9.7 x 4.4 mm
θJA = 26 °C/W

## Slide 15: Camaro LP887x-Q1 Family 4/6 CH
Features
AEC-Q100 Qualified for Automotive Applications (Grade 1: TA -40C to +125C)
Boost or Sepic converter with Integrated Power MOSFET
    Input Voltage Operating Range 3 V to 48 V
    Up to 45 V Output Voltage
    5.4 A Switching Current Limit
    Dynamic switching current limit for cold crank
    Switching Frequency 100 kHz to 2.2 MHz with the option of sync input
    Support Dual/Single phase operation
    Output voltage automatically discharged when boost is disabled
Thermal
    50 mΩ low rds on of SW FET
    VQFN-24(W) HotRod /PWP- 28 Package available
    Adaptive Voltage Control for Power Optimization
Low EMI/noise
    DRSS for ultra-low EMI
    Optimized switching slew rate
High-Precision Current Sinks
    4/6 channels * 150 mA LED output total current
    Current Matching 1%(typical), 2%@150mA, 3%@50mA
    Up to 16-bit LED Dimming Resolution
    Dimming Ratio 65,000:1 @ 152Hz PWM(100ns minimum pulse)
    Support Direct PWM, enhanced Phase shift PWM, Hybrid dimming and Analog dimming mode with external PWM input pin
  Full Protection and Diagnostic Features
    Support Power Line NFET for input OCP protection
    Soft Start Control for Vin transient
    1MHz I2C interface with CRC
    Open, Shorted, Short-to-GND LED Fault Detection
    Boost Output OVP and OCP, Input UVLO, OVP and OCP
    External Resistor Fault Errors
    Support Thermal warning and thermal shutdown
Applications
  Automotive Infotainment
  Automotive Instrument Clusters
  Smart Mirrors
  Heads-Up Displays (HUD)
  Central Information Displays (CID)
  Audio-Video Navigation (AVN)
Next-gen 4 / 6-ch x 150 mA Automotive LED Backlight Driver with Ultra-low EMI
Development

## Slide 16: Camaro LP889x-Q1 Family 4/6 CH
Features
AEC-Q100 Qualified for Automotive Applications (Grade 1: TA -40C to +125C)
Boost or Sepic converter with Integrated Power MOSFET
    Input Voltage Operating Range 3 V to 48 V
    Up to 45 V Output Voltage
    7.5 A Switching Current Limit
    Dynamic switching current limit for cold crank
    Switching Frequency 100 kHz to 2.2 MHz with the option of sync input
    Support Dual/Single phase operation
    Output voltage automatically discharged when boost is disabled
Thermal
    50 mΩ low rds on of SW FET
    VQFN-24(W) HotRod /PWP- 28 Package available
    Adaptive Voltage Control for Power Optimization
Low EMI/noise
    DRSS for ultra-low EMI
    Optimized switching slew rate
High-Precision Current Sinks
    4/6 channels * 150/200 mA LED output total current
    Current Matching 1%(typical), 2%@150mA, 3%@50mA
    Up to 16-bit LED Dimming Resolution
    Dimming Ratio 65,000:1 @ 152Hz PWM(100ns minimum pulse)
    Support Direct PWM, enhanced Phase shift PWM, Hybrid dimming and Analog dimming mode with external PWM input pin
  Full Protection and Diagnostic Features
    Support Power Line NFET for input OCP protection
    Soft Start Control for Vin transient
    1MHz I2C interface with CRC
    Open, Shorted, Short-to-GND LED Fault Detection
    Boost Output OVP and OCP, Input UVLO, OVP and OCP
    External Resistor Fault Errors
    Support Thermal warning and thermal shutdown
Applications
  Automotive Infotainment
  Automotive Instrument Clusters
  Smart Mirrors
  Heads-Up Displays (HUD)
  Central Information Displays (CID)
  Audio-Video Navigation (AVN)
Next-gen 4 / 6-ch x 150/200 mA Automotive LED Backlight Driver with Ultra-low EMI
Development
LP889x-Q1

## Slide 17: LP8867- Q1 / LP8869 - Q1
Benefits
Minimum system cost and PCB size with Integrated MOSFET
Good EMI performance with Spread Spectrum function
Save MCU resource with
  Power-Line FET control
  Automatic LED current reduction with external Temperature Sensor
Features
AEC-Q100 Qualified for Automotive Applications (Grade 1: TA -40C to +125C)
  4/3 x 120mA LED Driver for Automotive LCD Display
    High Dimming Ratio of 10 000:1 at 100 Hz
    Current Matching 1% (Typical)
    LED String Current up to 120 mA per Channel
    Outputs can be Combined Externally for Higher Current per String
Integrated Boost/SEPIC Converter for LED String Power
    Integrated SW FET with Up to 3A Switching Current Limit
    Input Voltage Operating Range 4.5 V to 40 V
    Output Voltage up to 45 V
    Switching Frequency 300 kHz to 2.2 MHz
    Switching Synchronization Input
    Spread Spectrum for Lower EMI
    Minimum Number of External Components
Protection and Fault Detection
    Power-Line FET Control for Battery Bus Protection
    Fault Output
    Input Voltage OVP, UVLO and OCP
    Boost OVP, SW OVP
    Open and Shorted LED Fault Detection
    Automatic LED Current Reduction With External Temperature Sensor
    Thermal Shutdown
HTSSOP-20 Package (PWP)
Applications
Backlight for:
  Automotive Infotainment
  Automotive Instrument Clusters
  Smart Mirrors
  Heads-Up Displays (HUD)
  Central Information Displays (CID)
  Audio-Video Navigation (AVN)

## Slide 18: LP8867C- Q1 / LP8869C - Q1
Benefits
Minimum system cost and PCB size with Integrated MOSFET
Good EMI performance with Spread Spectrum function
Features
AEC-Q100 Qualified for Automotive Applications (Grade 1: TA -40C to +125C)
  4/3 x 120mA LED Driver for Automotive LCD Display
    High Dimming Ratio of 10 000:1 at 100 Hz
    Current Matching 1% (Typical)
    LED String Current up to 120 mA per Channel
    Outputs can be Combined Externally for Higher Current per String
Integrated Boost/SEPIC Converter for LED String Power
    Integrated SW FET with Up to 3A Switching Current Limit
    Input Voltage Operating Range 4.5 V to 40 V
    Output Voltage up to 45 V
    Switching Frequency 300 kHz to 2.2 MHz
    Switching Synchronization Input
    Spread Spectrum for Lower EMI
    Minimum Number of External Components
Protection and Fault Detection
    Fault Output
    Input Voltage OVP, UVLO and OCP
    Boost OVP, SW OVP
    Open and Shorted LED Fault Detection
    Thermal Shutdown
HTSSOP-20 Package (PWP)
Applications
Backlight for:
  Automotive Infotainment
  Automotive Instrument Clusters
  Smart Mirrors
  Heads-Up Displays (HUD)
  Central Information Displays (CID)
  Audio-Video Navigation (AVN)

## Slide 19: LP8868/5-Q1
Benefits
High Brightness Support with
High Power Density Support Various Application
Dimming
Fast Response Support High Dimming Ratio Performance
Mixed Analog and PWM Dimming Method Accelerate the Dimming Performance
Features
AEC-Q100 Qualified for Automotive Applications (Grade 1: TA -40C to +125C)
Single Channel Current Sink
Output Current up to 4A / 2A
Analog, PWM, Hybrid Brightness Control Modes
Analog Dimming (128:1)
PWM Dimming (0.2us min. on time)
Hybrid Dimming (2000:1 in 20kHz PWM)
Boost/Buck-boost/Buck Power Stage Topology
Input Voltage Operating Range 4.5V to 65V
Integrated 150mΩ / 300mΩ NFET
NFET Current Limit: 4.5A / 2.5A
Switching Frequency 100 kHz to 2.2 MHz
Spread Spectrum for Lower EMI
  Protection and Diagnostic Features
  Cycle-by-cycle Current Limit
  LED Open
  Thermal Shutdown
  Fault Output
VSON-14/HVSSOP-12 Package
Applications
Backlight for:
Automotive Infotainment
Automotive Instrument Clusters
Smart Mirrors
Heads-Up Displays (HUD)
Central Information Displays (CID)
Audio-Video Navigation (AVN)
Buck
Boost
Buck/boost

## Slide 20: LP8866-Q1 / LP8866S-Q1
Benefits
High Brightness and Big Size LCD Panel Support with
  6 * 200/150mA LED Output
Good Cold cranking behavior with
  Input Voltage Operating Range 3 V to 48 V
Good EMI Performance with
  Phase Shifted LED Outputs
  Boost Converter Spread Spectrum
  Hybrid Dimming (Linear + PWM)
  Boost Synchronization Input
Ease Customer design with
  Resistor Configuration for PWM /Boost Frequency/LED Configuration/Dimming Mode
  Integrated Discharge Function
Features
AEC-Q100 Qualified for Automotive Applications (Grade 1: TA -40C to +125C)
Six High-Precision Current Sinks
    Output Current up to 200/150 mA/Channel
    Current Matching 1% (typical)
    Up to 16-bit LED Dimming Resolution
    Dimming Ratio 32,000:1 @ 152Hz PWM
    I2C, PWM Brightness Control Modes
    8 configurable LED strings configuration
    Automatically adjusts phase shift for number of LED strings
Boost Controller for LED String Power
    Input Voltage Operating Range 3 V to 48 V
    Switching Frequency 100 kHz to 2.2 MHz
    Boost SYNC input to set boost switching frequency from an external clock
    Spread Spectrum for lower EMI
    Adaptive Voltage Control for Power Optimization
    Output voltage automatically discharged when boost is disabled
  Full Protection and Diagnostic Features
    Open, Shorted, Short-to-GND LED Fault Detection
    Boost Output OVP and OCP
    Boost Input UVLO, OVP and OCP
    External Resistor Fault/Charge Pump Fault/CRC Errors
    VDD UVLO and Thermal Shutdown
HTSSOP-38 Package (DCP)
Applications
Backlight for:
  Automotive Infotainment
  Automotive Instrument Clusters
  Smart Mirrors
  Heads-Up Displays (HUD)
  Central Information Displays (CID)
  Audio-Video Navigation (AVN)

## Slide 21: LP8864-Q1 / LP8864S-Q1
Benefits
Features
AEC-Q100 Qualified for Automotive Applications (Grade 1: TA -40C to +125C)
Four High-Precision Current Sinks
    Output Current up to 200/150 mA/Channel
    Current Matching 1% (typical)
    Up to 16-bit LED Dimming Resolution
    Dimming Ratio 32,000:1 @ 152Hz PWM
    I2C, PWM Brightness Control Modes
    8 configurable LED strings configuration
    Automatically adjusts phase shift for number of LED strings
Boost Controller for LED String Power
    Input Voltage Operating Range 3 V to 48 V
    Switching Frequency 100 kHz to 2.2 MHz
    Boost SYNC input to set boost switching frequency from an external clock
    Spread Spectrum for lower EMI
    Adaptive Voltage Control for Power Optimization
    Output voltage automatically discharged when boost is disabled
  Full Protection and Diagnostic Features
    Open, Shorted, Short-to-GND LED Fault Detection
    Boost Output OVP and OCP
    Boost Input UVLO, OVP and OCP
    External Resistor Fault/Charge Pump Fault/CRC Errors
    VDD UVLO and Thermal Shutdown
HTSSOP-38 Package (DCP)
Applications
Backlight for:
  Automotive Infotainment
  Automotive Instrument Clusters
  Smart Mirrors
  Heads-Up Displays (HUD)
  Central Information Displays (CID)
  Audio-Video Navigation (AVN)
High Brightness and Big Size LCD Panel Support with
  4 * 200/150mA LED Output
Good Cold cranking behavior with
  Input Voltage Operating Range 3 V to 48 V
Good EMI Performance with
  Phase Shifted LED Outputs
  Boost Converter Spread Spectrum
  Hybrid Dimming (Linear + PWM)
  Boost Synchronization Input
Ease Customer Design with
  Resistor Configuration for PWM /Boost Frequency/LED Configuration/Dimming Mode
  Integrated Discharge Function

## Slide 22: LP8863-Q1
Benefits
High Brightness and Big Size LCD Panel Support with
  6*150mA LED output
Good Cold cranking behavior with
  Input Voltage Operating Range 3 V to 48 V
Good EMI Performance with
  Phase Shifted LED Outputs
  Boost Converter Spread Spectrum
  Hybrid Dimming (Linear + PWM)
  Boost Synchronization Input
Ease Customer Design with
  Resistor Configuration
  Automatic Detection of LED String Configuration
  Integrated Discharge Function
Features
AEC-Q100 Qualified for Automotive Applications (Grade 1: TA -40C to +125C)
Six High-Precision Current Sinks
    Output Current up to 150 mA/Channel
    Current Matching 1% (typical)
    Up to 16-bit LED Dimming Resolution
    Individual LED String Brightness Control
    Dimming Ratio 32,000:1 @ 152Hz PWM
Boost Controller for LED String Power
    Input Voltage Operating Range 3 V to 48 V
    Switching Frequency 300 kHz to 2.2 MHz
    Boost SYNC input
    Spread Spectrum for lower EMI
    Adaptive Voltage Control for Power Optimization
    Discharge function when boost is disabled
Extensive Protection Features
    Open and Shorted LED Fault Detection
    Boost Output OVP and OCP
    Boost Input UVLO, OVP and OCP
    VDD UVLO and Thermal Shutdown
Simple Configuration
    Resistor configuration for Boost Frequency, LED PWM Frequency and LED Current
    Automatic String Configuration Detection
    Automatically adjusts phase shift for number of LED strings
    I2C, SPI and PWM Brightness Control Modes
  HTSSOP-38 Package (DCP)
Applications
Backlight for:
  Automotive Infotainment, Instrument Clusters
  Smart Mirrors, Heads-Up Displays (HUD)
  Central Information Displays (CID)
  Audio-Video Navigation (AVN)

## Slide 23: Automotive LCD Bias Roadmap
TPS65150-Q1
Saber
TPS92100-Q1
Released
Development
Saber
Unipolar
Bipolar
AVDD, VCOM, VGH, VGL
Excellent AVDD output voltage accuracy: <1%
I 2C
TSSOP
4-CH
TPS65131-Q1
I 2C
QFN
2-CH
PAVDD, NAVDD
Independent enable pins for power up and down
Power save mode available at low load currents
Up to 85% efficiency
PAVDD, NAVDD, VGH, VGL, VCOM
8bits VCOM Calibrator with buffer
Supports power-up and -down sequencing
I2C interface with EEPROM
Peak Efficiency >90 % at VIN = 3.3V
PAVDD, NAVDD
8bits VCOM Calibrator with buffer
Supports power-up and -down sequencing
I2C interface with EEPROM
Peak Efficiency >90 % at VIN = 3.3V
I 2C
QFN
5-CH
I 2C
QFN
2-CH
System Architecture
Notes: a-Si (amorphous Silicon) is one of the most widely used, simple technology and low cost. It's PPI about 200.
IPS (In-Plane Switching) is the best all around panel type, but is more expensive. It supports a wide visual angle and good performance of color reduction.
LTPS (Low Temperature Polysilicon) panels consume lower power and support high resolution (>500 ppi).

## Slide 24: TPS65131-Q1
Dual Output Regulator
Input Voltage Range: 2.7 to 6V
  3.3V, 5V inputs
VPOS Boost Converter (PAVDD):
  VPOS: ~VIN to 15V
  1.4MHz Switching Frequency
  1.7A Minimum Current Limit
  Up to 89% Efficiency
VNEG Inverting B-B Converter (NAVDD)
  VNEG: ~15 to 2V
  1.4MHz Switching Frequency
  1.7A Minimum Current Limit
  Up to 81% Efficiency
Power-Save Mode for High Efficiency at Low Load Currents
Independent Enable Inputs for Power-Up and Power-Down Sequencing
Pin-selectable, forced Fixed-Frequency PWM Operation
Overvoltage Protection on Both Outputs
Small 4-mm × 4-mm QFN-24 Package (RGE)
AEC-Q100 Grade 2 n40c to 85c operating temp
TFT LCD Displays for Automotive
Infotainment, Cluster, Navigation
Rear Seat Entertainment
High efficient dual output device (total efficiency up to 85%)
High flexibility (independent enable pins…)
Low external component count for reduced overall BOM costs
Automotive qualified
bipolar (± AVDD)

## Slide 25: Auto Mini-Micro LED Driver Roadmap
LED# | About 200 | About 1,000 | About 10,000
I avg | 25mA | 10mA | 1mA
LED Pitch | 10mm | 2-5mm | 1mm
TLC69637-Q1
TLC69638-Q1
TLC69639-Q1
7-bit Dot Correction
16-bit PWM Resolution
17MHz SPI / CSI
Spread Spectrum
0.2V Vsat @30mA
UART/CAN over UPAC
TLC69697/8-Q1
FuSa
48ch
100 mA/ch
TLC69620-Q1
7-bit Dot Correction
16-bit PWM Resolution
12MHz SPI
0.35V Vsat @30mA
UART/CAN over UPAC
TLC69697-Q1
48ch
80 mA/ch
Sample
LP5860-Q1
LP5868-Q1
LP5866-Q1
Integrated SW FETs
8-bit Dot Correction
8/16-bit PWM Resolution
12MHz SPI
0.6V Vsat @75mA
UART/CAN over UPAC
LP5869-Q1
18ch x 11sw
80 mA/ch
Released
TLC69648-Q1
Integrated SW FETs
7-bit Dot Correction
16-bit PWM Resolution
12MHz SPI / CSI
0.2V Vsat @30mA
UART/CAN over UPAC
TLC69697/8-Q1
48ch x 4sw
80 mA/ch
Developing
LP5893-Q1
Integrated SW FETs
8-bit Dot Correction
16-bit PWM Resolution
12MHz CSI
Stackable mode
UART/CAN over UPAC
TLC69697/8-Q1
48ch x 16sw
40 mA/ch
Developing
LP5892-Q1
LP5891-Q1
Integrated SW FETs
8-bit Dot Correction
16-bit PWM Resolution
50MHz CCSI
Stackable mode 2x/4x
SPI over UPAC
LP5899-Q1
48ch x 16sw
20/40 mA/ch
Released
FuSa
Released
Higher Dot Current
Higher LED #
Notes: The background is that a market called body exterior freeform interactive signal display appears. What’s that??
Traditional Lighting is a pure functional application, request on/off the LED or adjust the brightness.
FISD added value to more intelligent applications, offering personalization, communication, and assistance for the driver
This figure provides the overview of popular exterior FISD application to help understand. For example, the grille is designed to shows smooth animation as a unique character, display closed to the handle warn the status to communicate with passenger.
Though There are many applications, they can be classified to 3 parts by the pixel pitch. it is the distance between adjacent LEDs.
///////
Fine Pitch FISD
For passerby, long distance, animation- （）
Mini LED FISD
For passenger, short distance, Video and text – (small display screen)
FISD personalization and communication purposes.

## Slide 26: TLC6963x-Q1
Part Number | TLC69639-Q1 | TLC69636-Q1 | TLC69633-Q1
 | TLC69638-Q1 | TLC69635-Q1 | TLC69632-Q1
 | TLC69637-Q1 | TLC69634-Q1 | TLC69631-Q1
Channel | 48-ch, 100mA | 24-CH, 100mA | 8-CH, 100mA
Package | HTSSOP-56 (14mm x 6mm) QFN-56 (8mm x 8mm) | HTSSOP-28 (9.7mm x 4.4mm) QFN-28 (4mm x 4mm) | SOT-14 (4.2mm x 2.0mm) QFN-14 (2.5mm x 2.5mm)
FuSa Augmented (ISO26262, ASIL-B)
FuSa Compliant (ISO26262, ASIL-B)
FuSa Capable
Channel: Short to GND | LOD | LSD | APS
Device: UVLO | ISET out of range | TSD
Communication: CRC | Time-out
Fail-safe Mode | OTP CRC | Oscillator Watchdog
Programmable Safety Zone | Automatic Faults Summarizing
LED Drivers Cascaded Daisy Chain Connection
UPAC
LED Driver
LED
Driver
LED
Driver
LED
Driver
LED
Driver
LED
Driver

## Slide 27: LP5891-Q1 Automotive 48x16 matrix LED driver with 16-bits PWM dimming and ultra low power
Separated VCC and VLED Power Supply
  VCC Voltage Range: 2.5V – 5.5V ( Recommend: 2.5/2.8V)
  VLEDR/G/B Voltage Range: 2.5V - 5.5V (R Recommend: 2.8V, B Recommend: 3.8V)
16 Integrated Line Scan Switches (NMOS)
  RDS(ON): 190 mohm (typ)
48 Constant-Current-Source Channels from 0.1 mA to 20mA
  Channel-to-channel, 0.5% (typ), 2% (max)
  Device-to-device, 0.5% (typ), 2% (max)
  Knee voltage: 0.3V @10mA(max)
  3-Bit (8 steps) Global Brightness Control
  8-Bit (256 steps) Color Brightness Control for each color group
Ultra Low Power Consumption
  Icc=5.5mA (5.4uA/pixel) with Vcc=2.8V @ 50MHz
  Intelligent Power Saving Mode (by channel)
  Dynamic Power Saving Mode (by device) Icc down to 2.4mA
  Active Power Saving Mode Icc down to 0.6mA
Maximum 16-Bit (65536 steps) PWM Grayscale Control
Built-in SRAM to support 48×16 LED Matrix With Single Device
High Speed 2-wire Communication Interface
  External Serial Data Transfer Clock: 50MHz
  Internal Clock Multiplier: 1× to 16x (up to 160MHz)
Common display issue solution
LED Open / Short Detection and Caterpillar Removal
Package: 9mmx9mm QFN-76
Features
Applications
Automotive Interior Light
Automotive Rear Light
Automotive Local Dimming Backlight
LP5891-Q1
Benefits
High accuracy constant current sources for enhanced uniformity
16-bit PWM resolution brings ultra smooth lighting effects
Low power consumption
Premium LED matrix performances
LP5891-Q1

## Slide 28: Universal Plug-in Augmented Connectivity (UPAC) ‒ LP5899-Q1 SPI-Compatible Connectivity for LP5891-Q1
Input voltage range: 2.5V to 5.5V
Diagnostics
  SPI CRC error detection
  SPI time out detection
  CCSI register data CRC detection
  CCSI data input stuck-at detection
  Oscillator fault detection
  OTP CRC error detection
  Fault pin report
Data ready interrupt
Operating ambient temperature (-40°C to 125°C)
Package:
  WSON-12 Wettable (3mm*3mm*0.8mm)
  SOT-14 (4.2mm*2mm*1.1mm)
Features
Benefits
Compatible with SPI controller
Reduced controller requirements with standard SPI interface and reduced CPU overhead
CCSI data integrity inspection
SPI compatible connectivity for LP5891-Q1
Applications

## Slide 29: Illuminating LED driver roadmap
Buck
Boost
Output Power
10W
50W
100W
TPS92200
TPS922054
Inductive Fast Dimming
TPS923610/1/2
Vout_max 30V
TPS61165
Vin max 18V
Topology
TPS922055
Inductive Fast Dimming
Spread Spectrum
20W
TPS923654*
Inductive Fast Dimming
TPS923655*
Inductive Fast Dimming
Spread Spectrum
TPS92201
TPS922052
Inductive Fast Dimming
TPS922053
Inductive Fast Dimming
Spread Spectrum
TPS923652*
Inductive Fast Dimming
TPS923653*
Inductive Fast Dimming
Spread Spectrum
TPS922050
Analog/PWM Dimming
TPS922051
Analog/PWM Dimming
TPS923651*
Analog/PWM Dimming
TPS923650*
Analog/PWM Dimming
TPS92401
4-dot controller
Power Save Mode
TPS92402
8-dot controller
Power Save Mode
LED dot controller
<7-V VIN max
<18-V VIN max
<30-V VIN max
>30-V VIN max
75W
Namtso
Buck
Namtso
Boost
Baikal
TPS92641 next gen
TPS923613
Vin_min 1.8V
TPS61169
Vin_max 5.5V
* Boost / Buck-Boost multi-topology

## Slide 30: TPS92205x / TPS92365x family
Topology | Buck | Buck | Boost / Buck-Boost | Boost / Buck-Boost
Power density | Vin 4.5-65V, Iout 2A/4A | Vin 4.5-65V, Iout 1A/2A | Vin 4.5-65V, Iout 2A/4A | Vin 4.5-65V, Iout 1A/2A
SW frequency | 0.1~2.2MHz with S.S. | 1MHz / 0.4MHz | 0.1~2.2MHz with S.S. | 1MHz / 0.4MHz
Analog Dim. Ratio | 256: 1 | 200:1 | 256: 1 | 200:1
PWM Min. On time | 150ns | 50ns | 150ns | 50ns
Hybrid Dimming | Yes | No | Yes | No
Protection Mechanism | Fault output [open drain] | / | Fault output [open drain] | /
 | LED Open | LED Open | LED Open / Short | LED Open / Short
 | Thermal Foldback, OVP | Thermal Shutdown, OVP | Thermal Foldback, OVP | Thermal Shutdown, OVP
Package | VSON-14, WSON-12 SOT-14, | WSON-8, SOT-8, MSOP-8 | VSON-14, WSON-12 SOT-14 | WSON-8, SOT-8, MSOP-8
TPS922052/3/4/5
TPS922050/1
TPS923652/3/4/5
TPS923650/1
2A/4A non-synchronous multi-topo LED drivers with up to 65V input voltage, featuring high power density illumination and fast LED current rising/falling time
Kanas

## Slide 31: TPS922052/3/4/5 2/4-A Buck LED Driver with flexible & enhanced dimming performance
4.5V to 65V wide input range
LED common anode connection
Integrated 150mΩ MOSFET with typical 3A / 6A current limit
Optional switching frequency: 100kHz to 2.2MHz
Spread spectrum for TPS922053 and TPS922055
Advanced dimming options:
  – Analog dimming (256:1)
  – Fast PWM dimming (150ns pulse width)
  – Hybrid and flexible dimming (2,000:1 at 20kHz PWM)
Full protection features:
  – LED open and short protection
  – Switching FET open and short protection
  – External component failure protection
  – Cycle-by-cycle current limit
  – Thermal shutdown
  – Fault output (open drain)
Configurable thermal foldback curve
VSON, WSON and SOT23 package options
Features
Benefits
Constant illumination:
  – Indoor, outdoor, professional lighting
  – Medical, surgical lighting
  – Projector, laser TV, printer, IP camera
Instant illumination:
  – Machine vision, camera flash
  – Fire alarm, strobe
CC and CV source:
  – LCD backlighting
  – Battery charging
  – TEC control
Applications
High power density support various application
Fast response supports high contrast ratio
Multiple dimming methods enable high dimming performance
Buck Topology optimized pinout and layout for single layer PCB
Spread spectrum relaxes system EMI filter
Fault output for fast system fault handling
Thermal foldback brings more system reliability
31

## Slide 32: TPS923652/3/4/5 2/4-A Boost / Buck-Boost LED Driver with flexible & enhanced dimming performance
4.5V to 65V wide input range
LED common cathode connection
Integrated 150mΩ MOSFET with typical 3A / 6.5A / 8.5A current limit
Optional switching frequency: 100kHz to 2.2MHz
Spread spectrum for TPS923653 and TPS923655
Advanced dimming options:
  – Analog dimming (256:1)
  – Fast PWM dimming (150ns pulse width)
– Hybrid and flexible dimming (2,000:1 at 20kHz PWM)
Full protection features:
  – LED open and short protection
  – Switching FET open and short protection
  – External component failure protection
  – Cycle-by-cycle current limit
  – Thermal shutdown
  – Fault output (open drain)
Configurable thermal foldback curve
VSON, WSON and SOT23 package options
Features
Benefits
Applications
32
High power density support various application
Fast response supports high contrast ratio
Multiple dimming methods enable high dimming performance
Boost Topology optimized pinout and layout for single layer PCB
Spread spectrum relaxes system EMI filter
Fault output for fast system fault handling
Thermal foldback brings more system reliability
Constant illumination:
  – Indoor, outdoor, professional lighting
  – Medical, surgical lighting
  – Projector, laser TV, printer, IP camera
Instant illumination:
  – Machine vision, camera flash
  – Fire alarm, strobe
CC and CV source:
  – LCD backlighting
  – Battery charging
  – TEC control

## Slide 33
TPS922050/1 65-V 1-A/2-A Buck LED Driver with Analog/PWM Dimming
4.5V to 65V wide input range
LED common anode connection
Integrated 300mΩ MOSFET:
  – Typical current limit (1.6A / 3.2A)
  – Switching frequency (400kHz / 1MHz)
Advanced dimming options:
  – Analog dimming (200:1)
  – Fast PWM dimming (50ns pulse width)
Full protection features:
  – LED open and short protection
  – Switching FET open and short protection
  – External component failure protection
  – Cycle-by-cycle current limit
  – Thermal shutdown
Package: WSON-8, HVSSOP-8, SOT583
Features
Benefits
Constant illumination:
  – Indoor and outdoor lighting
  – Appliance lighting
  – Cold/warm WLED lighting
  – Emergency and signage lighting
  – Security floodlight
  – LED bulb and lamp
  – LCD backlight
Instant illumination:
  – Machine vision and camera flash
  – Fire alarm and strobe
Applications
High power density support various application
Short pulse response supports high dimming frequency and high contrast ratio
Buck Topology optimized low number pinout and layout for single layer PCB
Fault protection and thermal shutdown for essential reliability

## Slide 34
TPS923650/1 65-V 1-A/2-A Boost/Buck-Boost LED Driver with Analog/PWM Dimming
4.5V to 65V wide input range
LED common cathode connection
Integrated 300mΩ MOSFET:
  – Typical current limit (1.6A / 3.2A)
  – Switching frequency (400kHz / 1MHz)
Advanced dimming options:
  – Analog dimming (200:1)
  – Fast PWM dimming (50ns pulse width)
Full protection features:
  – LED open and short protection
  – Switching FET open and short protection
  – External component failure protection
  – Cycle-by-cycle current limit
  – Thermal shutdown
Package: WSON-8, HVSSOP-8, SOT583
Features
Benefits
High power density support various application
Short pulse response supports high dimming frequency and high contrast ratio
Buck Topology optimized low number pinout and layout for single layer PCB
Fault protection and thermal shutdown for essential reliability
Constant illumination:
  – Indoor and outdoor lighting
  – Appliance lighting
  – Cold/warm WLED lighting
  – Emergency and signage lighting
  – Security floodlight
  – LED bulb and lamp
  – LCD backlight
Instant illumination:
  – Machine vision and camera flash
  – Fire alarm and strobe
Applications

## Slide 35: TPS92401 4-Channel 5-A LED Dot-Controller with Integrated FET and Advanced Dimming
Wide Input Voltage Range: 4.5V to 65V
Common Cathode / Common Anode
4 Integrated LED Bypass Switches
  5A Max Continuous Current
Integrated 16-bit PWM Generator and SPI Interface
  Programmable PWM Frequency Up to 60kHz
  Programmable PWM Slew Rate and Shifting
  Support SPI Daisy Chain / Star Connection
Protection & Diagnostics
  Programmable LED Open Protection
  LED Short / Resistive FET Detection
  Thermal Warning
Support Power Save Mode
Support Stacked Configurations
Operating Ambient Temperature (-40°C to 125°C)
Package: VQFN-36
Features
Benefits
Extremely power efficient for ~5A LED pixel-level dot lighting control scenario
>20kHz PWM frequency support for no flickering in high speed camera and audible noise free
4-channel device for single-layer easy routing and flexible connection
Best compatible with TPS92205x and TPS92640/1 LED drivers
Stage Lighting
Surgical Lighting
Machine Vision Illumination
3D Printing
Atmosphere Lighting
Applications

## Slide 36: TPS92402 8-Channel 2.5-A LED Dot-Controller with Integrated FET and Advanced Dimming
Wide Input Voltage Range: 4.5V to 65V
Common Cathode / Common Anode
4 Integrated LED Bypass Switches
  2.5A Max Continuous Current
Integrated 16-bit PWM Generator and SPI Interface
  Programmable PWM Frequency Up to 60kHz
  Programmable PWM Slew Rate and Shifting
  Support SPI Daisy Chain / Star Connection
Protection & Diagnostics
  Programmable LED Open Protection
  LED Short / Resistive FET Detection
  Thermal Warning
Support Power Save Mode
Support Stacked Configurations
Operating Ambient Temperature (-40°C to 125°C)
Package: VQFN-36
Features
Benefits
Extremely power efficient for ~2.5A LED pixel-level dot lighting control scenario
>20kHz PWM frequency support for no flickering in high speed camera and audible noise free
8-channel device for single-layer easy routing and flexible connection
Best compatible with TPS92205x and TPS92640/1 LED drivers
Stage Lighting
Surgical Lighting
Machine Vision Illumination
3D Printing
Atmosphere Lighting
Applications

## Slide 37: TPS922152/3/4/5 (Namtso) High Voltage Buck LED Driver with Accurate Dimming
Supply Voltage Range: 4.5 to 18V
Common Anode
2-Ω, 1-Apeak MOSFET Gate Driver
Optional Control Mode:
  Adaptive Off-Time (TPS922152)
  Hysteresis Peak-Current (TPS922153)
  ZCS Quasi-Resonant Transition (TPS922154)
  ZVS True Quasi-Resonant (TPS922155)
Switching Frequency: 50kHz~2.2MHz
Mixed Dimming Option:
  Analog Dimming (1000:1)
  PWM Dimming (50ns pulse width)
Protection
  LED Open / Short
  Sense Resistor Open / Short
  Cycle by Cycle Current Limit
  Fault Output (Open Drain)
Operating Ambient Temperature(-40°C to 125°C)
Package: SOIC-8, SOT583
Features
Benefits
Industrial and Commercial Lighting
Indoor and Outdoor Lighting
Fire Alarm and Strobe
LCD TV/Display Backlight
LED Driver Module
LED Bulb/Lamp
Applications
Supports wide dc bus voltage and LED string voltage up to >100V
Enables simple layout with low number of external components
Multiple control modes for variable system needs
Quasi-resonant switching allows high frequency and high efficiency
Accurate analog dimming enables high dimming ratio and accuracy
Fast PWM dimming enables high dimming frequency and high dimming ratio
Low output ripple eliminates flickering at low brightness
Compatible with GaN power stage, such as LMG362x
37
Development

## Slide 38: TPS923752/3/4/5 (Namtso) High Voltage Boost/SEPIC LED Driver with Accurate Dimming
38
Development
Supply Voltage Range: 4.5 to 18V
2-Ω, 1-Apeak MOSFET Gate Driver
Optional Operation Mode:
  Adaptive Off-Time Boost (TPS923752)
  Adaptive Off-Time SEPIC (TPS923753)
  ZCS Quasi-Resonant Transition (TPS923754)
  ZVS True Quasi-Resonant (TPS923755)
Switching Frequency: 50kHz~2.2MHz
Mixed Dimming Option:
  Analog Dimming (1000:1)
  PWM Dimming (50ns pulse width)
Protection
  LED Open / Short
  Sense Resistor Open / Short
  Cycle by Cycle Current Limit
  Fault Output (Open Drain)
Operating Ambient Temperature(-40°C to 125°C)
Package: SOIC-8, SOT583
Features
Benefits
Industrial and Commercial Lighting
Indoor and Outdoor Lighting
Fire Alarm and Strobe
LCD TV/Display Backlight
LED Driver Module
LED Bulb/Lamp
Applications
Supports wide dc bus voltage and LED string voltage up to >100V
Enables simple layout with low number of external components
Multiple control modes for variable system needs
Quasi-resonant switching allows high frequency and high efficiency
Accurate analog dimming enables high dimming ratio and accuracy
Fast PWM dimming enables high dimming frequency and high dimming ratio
Low output ripple eliminates flickering at low brightness
Compatible with GaN power stage, such as LMG362x

## Slide 39: 1-/1.5-A High Efficiency Synchronous Buck LED Driver
Input Voltage Range: 2.5V to 5.5V
0.1-V to VIN output voltage range
Up to 1-/1.5-A continuous output current
  Integrated 200/160-mOhm HS/LS FET
  Current Limit: 1.5-/2-A
1.5-MHz switching Frequency
100% mode operation
Analog Dimming with 1%-100% range
A-version: Power save mode for light load efficiency
Protection
  Cycle by cycle current limit
  LED Open / Short
  Thermal Shutdown
Operating Ambient Temperature(-40°C to 85°C)
Package: SOT563, WSON
Features
Benefits
Video Doorbell
IP network camera flash / illumination
Battery-powered device flash / illumination
General Illumination
Applications
High efficiency for battery application
Both analog dimming supported to maximize dimming performance
TPS92201(A)

## Slide 40: TPS92200 4-30V/1.5-A Synchronous Buck LED Driver with Flexible Dimming Options
4V to 30V Wide Input Range
Integrated 150m/90m MOSFETs for 1.5A Continuous Output Current
1MHz Switching Frequency
Ultra-Low Shutdown Current: 1-μA
Ultra-Low Output Discharge Current from Load: 1-μA
Maximum Duty Cycle up to 99%
Flexible Dimming Options for different applications:
  TPS92200D1: PWM Dimming with Digital Input and Analog Dimming with Analog Input
  TPS92200D2: Analog Dimming with Digital Input
Ultra-low and Accurate FB Voltage: 100mV/+-3mV
Peak Current mode with Internal Compensation
Full Protections:
  LED Open-Load Protection with Maximum Duty ON
  LED+ Short to GND
  LED+ / LED- Short Circuitry
  Sense Resistor Open/ Short Protection
  Thermal Shutdown
SOT23-6 (2.8 x 2.9 mm), VQFN-HR-6 (1.5 x 2 mm)
Features
Benefits
Video Surveillance IR LED Driver
Facial Recognition IR LED Driver
Stage Lighting LED Driver
General Industrial and Commercial Illumiantion
AA or Li-ion Battery Charger
Applications
Ultra-low FB voltage for higher Efficiency
Ultra-low Shutdown Current (<1uA)
Flexible Dimming Options for Various Applications
Ultra-low Output Discharge Current help to Save An Output Diode for Charger Application
Small and Few external component count to optimize board space and cost
40
Device | Dimming Type | Dimming Input Type
TPS92200D1 | PWM Dimming | Digital Signal (frequency: 100Hz – 2kHz)
 | Analog Dimming | Analog Voltage (amplitude: 0.65-1.2V)
TPS92200D2 | Analog Dimming | Digital Signal (frequency: 20kHz – 200kHz)

## Slide 41: TPS61165 High Brightness White LED Driver in 2mm x 2mm WSON package
Wide Input Voltage Range: 3 -18V
38-V Open LED Protection
Up to 90% Efficiency
200-mV Reference Voltage With 2% Accuracy
Down to 1% Dimming Brightness
1.2-A Switch FET With 1.2-MHz Switching Frequency
One-Wire Control Interface (EasyScale™)
2.0 mm*2.0 mm WSON-6 Package with Thermal Pad and SOT-23 Package
Features
Benefits
Smart Phones
Tablets and Gaming Tablets
Home Automation Panels
Home Appliance User Interface
Portable/ Small Media Form Factor Displays
EPOS
Handheld Medical Equipment
Thermostat Display
Blood Glucose Meters
Video Surveillance Camera
Applications
Works with different power sources ( Industrial Rail, Li-ion Battery)
Smooth Brightness Transition
1% dimming ration can covers day/night ambient brightness conditions
High Efficiency help to increase battery endurance time
Small package for compact solutions and industrial applications
41

## Slide 42
Sample now
Single-channel Synchronous Boost LED Driver
Supply Voltage Range: 2.5V-5.5V
High efficiency Synchronous Boost with 280mΩ LSFET/600mΩ HSFET
High Precision PWM-to-analog Dimming Resolution up to 1000:1
1.8/2.3A Switch Current Limit
24.5V/30V Max Output Voltage
400k/1.2MHz Switching Frequency to with Small Size Inductor
Compatible with 1.2V I/O
Internal Bootstrap Capacitor
Internal Compensation
OVP/OCP/FB short-to-GND Protection
Package:
  1.6mm*1.6mm SOT563-6
  2mm*2mm WSON-6
Features
Benefits
LCD backlighting
  Smartphone and tablet
  Handheld data terminals (EPOS)
  Thermostat display
  PDA, handheld computer and GPS receiver
  Portable media player, portable TV and eBook
General illumination
  IP camera
  Flashlight
Applications
Save Schottky diode for smaller solution size and lower BOM cost
Small chip / cap / inductor size for mobile applications
Unique PWM dimming function allows higher brightness dynamic range without additional cost
TPS923610/1/2 (NEMO)

## Slide 43: RGB LED Driver
1 to 12 LED dots
8-bit PWM
1-MHz I2C
8-bit Analog
Auto animation
WCSP
DFN
9 to 36 LED dots
12-bit PWM
400-kHz I2C
Group control
QFN
18 to 198 LED dots
16-bit PWM
1-MHz I2C
QFN
8-bit Analog
TSSOP
Group control
8 / 16 LED channels
16-bit PWM
1-MHz I2C
QFN
TSSOP
Stackable
12-MHz SPI
LP581x
LP5817 / 6 / 5 / 4 / 3 / 2 / 1 / 0
LP50xx
LP5036 / 30 / 24 / 18 / 12 / 09
LP586x (T)
LP5860T / 8T / 7 / 6T / 4 / 2 / 1T
TLC59116
TLC59108 / 16
LED dot/channel
Dimming
Interface
Package
Function
Boost
TSSOP
5.5V
5.5V
5.5V
17V
Vout

## Slide 44: RGB LED Driver Roadmap
Number of LEDs
1-4 LEDs
5-12 LEDs
13-70 LEDs
71-400 LEDs
LP5811
4 channel
Integrated sync. boost
LP5813
4x3 matrix
Integrated sync. boost
LP5812
4x3 matrix
LP5009/12
9/12 channel
LP5018/24/30/36
18 -36 channel
LP5861 (T)
18 channel
T-version: 120mA/ch
LP5862
18x2 matrix
LP5864
18x4 matrix
LP5866/8/0 (T)
18x6/8/11 matrix
T-version: 100mA/ch
LP5867
7x6 matrix
WCSP package
Released
New release
In development/definition
LP5816/7
4/3 channel
LP5814/5
4/3 channel
Auto Animation, InstaBlink
LP5562
4 channel
LP5569
9 channel w/ charge pump
LP55281
12 channel
Integrated sync. boost
LP5521
3 channel w/ charge pump
LP5810
4 channel
Auto Animation
TLC59116
16 channel
VLED_max 17V
Moomin
48 channel
Tetris
18x13 matrix
Tetris Plus
33x13 matrix
Notes: Mark spread spectrum
RGB & ILLM one-page guild

## Slide 45: LP581x Family Introduction
LP581x
RGB LED driver family for up to 12 LED dots optional equipped with sync boost, auto animation control, and charging indication
Maximized battery life ─ down to 500uA operation current, 94% efficiency sync. boost
Optimize solution cost and size ─ Time-cross-multiplexing (TCM) matrix architecture
Free MCU real-time bus load ─ auto animation control with register configuration
InstaBlink™ Indication ─ Instant LED blinking via STAT pin control
LP581x value propositions
LOD / LSD
External SYNC
LP5810
DSBGA-9 (1.4 x 1.4mm)
WSON-8 (3 x 3mm)
Auto Animation
4 LEDs
Linear
LOD / LSD
External SYNC
LP5811
DSBGA-12 (1.8 x 1.4mm)
WSON-12 (3 x 3mm)
Auto Animation
4 LEDs
1.6A Sync Boost
LOD / LSD
External SYNC
LP5812
DSBGA-9 (1.4 x 1.4mm)
WSON-8 (3 x 3mm)
Auto Animation
4x3 = 12 LEDs
Linear
LOD / LSD
External SYNC
LP5813
DSBGA-12 (1.8 x 1.4mm)
WSON-12 (3 x 3mm)
Auto Animation
4x3 = 12 LEDs
1.6A Sync Boost
LP5814/I
DSBGA-8 (1.4 x 0.8mm)
SOT-8 (1.6 x 2.1mm)
Auto Animation
4 LEDs
Linear
LP5815
DSBGA-8 (1.4 x 0.8mm)
SOT-8 (1.6 x 2.1mm)
Auto Animation
3 LEDs
Linear
LP5816
DSBGA-8 (1.4 x 0.8mm)
SOT-8 (1.6 x 2.1mm)
4 LEDs
Linear
LP5817
DSBGA-8 (1.4 x 0.8mm)
SOT-8 (1.6 x 2.1mm)
3 LEDs
Linear
InstaBlink
InstaBlink

## Slide 46
Battery powered applications: E-tag, Smart watch, E-Cigarettes, Wearables
Smart speaker
Router and switches
Internet-of-Things (IOT)
Handheld device
LP5810/2
Supply voltage range: 2.7V – 5.5V
Time-cross-multiplexing (TCM) dot matrix
  Up to 12 LEDs (4 RGB LEDs) with individual control
  Current source/sink capability: 50mA when Vcc > 3.3V
  Average LED current: 4-dot: 50mA(Max.), 12-dot: 12.5mA(Max.)
  6kHz multiplexing frequency to avoid visual flicker
Ultra-low power consumption
  Standby current: 2uA(Typ.), 4uA(Max.)
  Operation current in normal mode: 0.5mA(Typ.)
  Flexible dimming control
  PWM dimming: 8-Bit, Gamma correction: 256 steps, 24kHz Freq.
  Analog dimming: 8-Bit
1MHz I2C interface, 4 P/N to support up to 4 devices used with one I2C bus
Logic pin power rail: 1.8V / 3.3V / 5V
Autonomous control: Auto breathing and blinking
LED open/short detection
Operating temperature range: -40°C ~ +85°C
Package: DSBGA-9 (1.43mm x 1.43mm), WSON-8 (3mm x 3mm)
Features
Benefits
Applications
Low supply voltage and Boost enable battery-powered applications (AA battery, Coin cell, Li-ion)
Time-cross-multiplexing(TCM) scheme saves total system PCB size and PCB traces
Ultra-low Iq saves system power and extends battery life
Flexible dimming control for smooth LED lighting patterns
Autonomous control offloads MCU bandwidth
4/12 LED Dots I2C RGB LED Driver With Auto Animation Control
RTM
LP5812
VCC
SCL
OUT
0
OUT1
OUT2
OUT3
1uF
2.7V
-
5.5V
D1
D2
D3
D4
GND
SYNC/INT
SDA
OFF
ON

## Slide 47
Battery powered applications: E-tag, Smart watch, E-Cigarettes, Wearables
Smart speaker
Router and switches
Internet-of-Things (IOT)
Handheld device
LP5811/3
Supply voltage range: 0.5V – 5.5V (Powering up from 1.8V)
Vout up to 5.5V for Boost
Time-cross-multiplexing (TCM) dot matrix
  Up to 12 LEDs (4 RGB LEDs) with individual control
  Current source/sink capability: 50mA when Vcc > 3.3V
  Average LED current: 4-dot: 50mA(Max.), 12-dot: 12.5mA(Max.)
  6kHz multiplexing frequency to avoid visual flicker
Ultra-low power consumption
  Shutdown current: 0.2uA(Typ.), 2uA(Max.)
  Standby current: 3uA(Typ.), 5uA(Max.)
  Operation current in normal mode: 0.5mA(Typ.)
  Flexible dimming control
  PWM dimming: 8-Bit, Gamma correction: 256 steps, 24kHz Freq.
  Analog dimming: 8-Bit
1MHz I2C interface, 4 P/N to support up to 4 devices used with one I2C bus
Logic pin power rail: 1.8V / 3.3V / 5V
Autonomous control: Auto breathing and blinking
LED open/short detection
Operating temperature range: -40°C ~ +85°C
Package: DSBGA-12 (1.84mm x 1,43mm), WSON-12 (3mm x 3mm)
Features
Benefits
Applications
Low supply voltage and Boost enable battery-powered applications (AA battery, Coin cell, Li-ion)
Time-cross-multiplexing(TCM) scheme saves total system PCB size and PCB traces
Ultra-low Iq saves system power and extends battery life
Flexible dimming control for smooth LED lighting patterns
Autonomous control offloads MCU bandwidth
47
4/12 LED Dots I2C Synchronous Boost RGB LED Driver With Auto Animation Control
RTM

## Slide 48: LP5814 4 - CH RGBW LED driver with auto animation
Supply Voltage Range: 2.5V-5.5V
VLED up to 5.5V
4-CH RGBW LED driver
Current sink capability: max 51mA
  Ultra-low power consumption
    Shutdown current: 0.1uA(Typ.), 0.3uA(Max.)
    Standby current: 26uA(Max.)
  Dimming control
    Individual PWM dimming: 23kHz, 8-bit
    Individual analog dimming: 8-bit
1MHz/400kHz I2C interface
Autonomous animation control
Compatible with 1.8V I/O
ESD: 4kV HBM, 1.5kV CDM
Package: 1.6mm*2.1mm SOT583, 1.36mm*0.8mm WCSP-8 with 0.35mm pitch
Features
RGB Indicator
E-cigarette
Router and Access point
Smart Home Appliance
TWS/Earbuds
Applications
Benefits
Ultra-low Iq saves system power and extends battery life
Autonomous control offloads MCU bandwidth
>20KHz dimming frequency to eliminate audible noise
LP5814
3V~5.5V

## Slide 49: LP5815 3 - CH RGB LED driver with auto animation and controllable InstaBlink
Supply Voltage Range: 2.5V-5.5V
VLED up to 5.5V
3 - CH RGB LED driver
Controllable InstaBlink
Current sink capability: max 51mA
  Ultra-low power consumption
    Shutdown current: 0.1uA(Typ.), 0.3uA(Max.)
    Standby current: 26uA(Max.)
  Dimming control
    Individual PWM dimming: 23kHz, 8-bit
    Individual analog dimming: 8-bit
1MHz/400kHz I2C interface
Autonomous animation control
Compatible with 1.8V I/O
ESD: 4kV HBM, 1.5kV CDM
Package: 1.6mm*2.1mm SOT583, 1.36mm*0.8mm WCSP-8 with 0.35mm pitch
Features
RGB Indicator
E-cigarette
Router and Access point
Smart Home Appliance
TWS/Earbuds
Applications
Benefits
Instant blinking via STAT pin control
Ultra-low Iq saves system power and extends battery life
Autonomous control offloads MCU bandwidth
>20KHz dimming frequency to eliminate audible noise
3V~5.5V
LP5815
Notes: InstaBlink – instant blinking

## Slide 50: LP5816 4 - CH RGBW LED driver
Supply Voltage Range: 2.5V-5.5V
VLED up to 5.5V
4-CH RGBW LED driver
Current sink capability: max 51mA
  Ultra-low power consumption
    Shutdown current: 0.1uA(Typ.), 0.3uA(Max.)
    Standby current: 26uA(Max.)
  Dimming control
    Individual PWM dimming: 23kHz, 8-bit
    Individual analog dimming: 8-bit
1MHz/400kHz I2C interface
Automatically fade in and fade out
Compatible with 1.8V I/O
ESD: 4kV HBM, 1.5kV CDM
Package: 1.6mm*2.1mm SOT583, 1.36mm*0.8mm WCSP-8 with 0.35mm pitch
Features
RGB Indicator
E-cigarette
Router and Access point
Smart Home Appliance
TWS/Earbuds
Applications
Benefits
Ultra-low Iq saves system power and extends battery life
>20KHz dimming frequency to eliminate audible noise
LP5816
3V~5.5V

## Slide 51: LP5817 3 - CH RGB LED driver
Supply Voltage Range: 2.5V-5.5V
VLED up to 5.5V
3 - CH RGB LED driver
Current sink capability: max 51mA
  Ultra-low power consumption
    Shutdown current: 0.1uA(Typ.), 0.3uA(Max.)
    Standby current: 26uA(Max.)
  Dimming control
    Individual PWM dimming: 23kHz, 8-bit
    Individual analog dimming: 8-bit
1MHz/400kHz I2C interface
Automatically fade in and fade out
Compatible with 1.8V I/O
ESD: 4kV HBM, 1.5kV CDM
Package: 1.6mm*2.1mm SOT583, 1.36mm*0.8mm WCSP-8 with 0.35mm pitch
Features
RGB Indicator
E-cigarette
Router and Access point
Smart Home Appliance
TWS/Earbuds
Applications
Benefits
Ultra-low Iq saves system power and extends battery life
>20KHz dimming frequency to eliminate audible noise
3V~5.5V
LP5817

## Slide 52: LP586x(T) Family Introduction
11 × 18 LED (T: high-current) LED matrix driver with 8-bit analog and 8-/16-bit PWM dimming
Premium visual effect: 8 bits analog dimming and 8/16 bits PWM dimming
Flexible interface options: I2C (1-MHz) and SPI (12-MHz)
Solution cost and size: Time-multiplexing architecture and integrated de-ghosting
High refresh rate: auto-increment function and individual LED dot register
Benefits for matrix LED Application
11 x 18 Matrix
SPI&I2C Interface
LP5860 (T)
5mm x 5mm QFN-40
8-bit DC
16-bit PWM dim
T for > 100mA/ch
SRAM
LOD/
LSD
8 x 18 Matrix
SPI&I2C Interface
LP5868 (T)
5mm x 5mm QFN-40
8-bit DC
16-bit PWM dim
T for > 100mA/ch
SRAM
LOD/
LSD
6 x 18 Matrix
SPI&I2C Interface
LP5866 (T)
5mm x 5mm QFN-40
9.7mm x 4.4mm TSSOP
8-bit DC
16-bit PWM dim
T for > 100mA/ch
SRAM
LOD/
LSD
4 x 18 Matrix
SPI&I2C Interface
LP5864
4mm x 4mm QFN-32
8-bit DC
16-bit PWM dim
SRAM
LOD/
LSD
2 x 18 Matrix
SPI&I2C Interface
LP5862
4mm x 4mm QFN-32
9.7mm x 4.4mm TSSOP
8-bit DC
16-bit PWM dim
SRAM
LOD/
LSD
1 x 18 Multi-ch
SPI&I2C Interface
LP5861 (T)
4mm x 4mm QFN-32
8-bit DC
16-bit PWM dim
T for > 100mA/ch
SRAM
LOD/
LSD

## Slide 53: LP586x(T)
18 Constant Current Sink with N Switches:
  LP5861(T): N=1: drive 18 LED dots or 6 RGB pixels.
  LP5862: N=2: drive 36 LED dots or 12 RGB pixels.
  LP5864: N=4: drive 72 LED dots or 24 RGB pixels.
  LP5866(T): N=6: drive 108 LED dots or 36 RGB pixels.
  LP5868(T): N=8: drive 144 LED dots or 48 RGB pixels.
  LP5860(T): N=11: drive 198 LED dots or 66 RGB pixels.
Operating Voltage Range: VCC/VLED Range: 2.7V to 5.5V; VIO Range: 1.8V to 5V power rails
Constant Current Sinks with High Precision:
  0.1-50 mA Maximum per current sink when VCC ≥ 3.3V
  0.1-100 mA Maximum per current sink for T versions only when VCC ≥ 3.3V
  Device-to-Device Error: ±5%; Channel-to-Channel Error: ±5%;
Flexible Dimming Options:
  Individual ON/OFF Control for Each Channel
  Analog Current Gain Control
    Global 3-bits Maximum Current(MC) Setting without Ext. Resistor
    3 Groups of 7-bits Color Current(CC) Setting
    Individual 8-bits Dot Current(DC) Setting
  Audible Noise Free (>20KHz) PWM Control
    Global 8-bits PWM for Global Dimming
    3 Programmable Groups of 8-bits PWM Dimming
    Individual 8-bits/16bits PWM for Each LED Dot
  Full Addressable SRAM for Minimum Data Volume
Ultra low quiescent current
  Shutdown Mode: 2uA (max.) when EN Low.
  Standby Mode: 10uA (max.) when CHIP_EN Low (data retained).
  Optional Interface: Up to 1MHz I2C, Up to 12MHz SPI.
  LED open/short detection
De-ghost, caterpillar removal, Low-brightness Compensation, low LED reverse voltage
Features
  High integration: (18xN) matrix structure up to 198 LEDs
  Highest dimming resolution: 16 bits (>20KHz) PWM dimming, 8 bits individual analog dimming
Ease of design: ‘True programmable group control’, ‘Minimum uC’s loadings’ and ‘Free of Matrix issues’
Benefits
  LED animation and indication for:
    Keyboard, mouse, and gaming accessories
    Major and smart home appliances
    Smart speaker, wired and wireless speaker
    Audio mixer, DJ equipment, and broadcast
    Access equipment, switches, and servers
  Constant current sinks for optical module
Applications
Nx18 LED Matrix Driver with 8-bit Analog and 8-/16-bit PWM Dimming
Package:
  QFN-32, 4x4mm(0.4mm pitch) --- LP5861(T), LP5862, LP5864
  QFN-40, 5x5mm(0.4mm pitch) --- LP5866(T), LP5868(T), LP5860(T)
  TSSOP-38, 9.7x4.4mm(0.5mm pitch) --- LP5866, LP5862

## Slide 54: LP5867WCSP 7×6 Matrix LED Driver
12 Constant Current Sink with N Switches
  LP5861: N=1: drive 6 LEDs
  LP5862: N=2: drive 12 LEDs
  LP5864: N=4: drive 36 LEDs
  LP5867: N=7: drive 42 LEDs
Operating Voltage Range:
  VCC/VLED Range: 2.7V to 5.5V
  VIO Range: 1.8V to 5V power rails
Constant Current Sinks with High Precision:
  1-50 mA Maximum per Channel when VCC ≥ 3.3V
  Device-to-Device Error: ±5%; Channel-to-Channel Error: ±5%;
Flexible Dimming Options:
  Individual ON/OFF Control for Each Channel
  Analog Current Gain Control
    3-bits Maximum Current Setting without Ext. Resistor
    3x7-bits Current Setting for Each Color Group
    8-bits Individual Current Setting for Each Channel
  Audible Noise Free (>20KHz) PWM Control (125KHz/62.5KHz)
    8-bits Master PWM for Global Brightness Control
    3x8-bits Bank PWM for Programmable Group Control
    8-bits/16bits Individual PWM for Each Channel
  Full Addressable SRAM for Minimum Data Volume
Ultra low quiescent current
  Shutdown Mode:
    1uA (max.) when EN Low.
    10uA (max.) when CHIP_EN Low (data retained).
  Optional Interface: Up to 1MHz I2C, Up to 12MHz SPI.
  LED open/short detection
Deghosting, caterpillar removal, Low-brightness Compensation, low LED reverse voltage
Package:
  WCSP-24, 2.5x1.8mm(0.4mm pitch), Ball Diameter 180um
Features
Benefits
  Small package: 2.5x1.75mm (0.4mm pitch)
  Two PCB layer supported
  High integration: (7xN) matrix structure up to 42 LEDs for single chip.
  Highest dimming resolution: with up to 16 bits (>20KHz) PWM dimming, 8 bits per channel analog dimming
Easy of Design: with ‘Programmable group dimming’ function and ‘Minimum data volume’ design

## Slide 55
Operating Voltage Range:
  Vcc Range: 2.7V to 5.5V
  EN, SDA and SCL pins compatible with 1.8V, 3.3V and 5V Power rails
  Output Maximum Voltage: 6V
Constant Current Sinks with High Precision
  25.5 mA Maximum per Channel when VCC in full range
  35 mA Maximum per Channel when VCC ≥ 3.3V
  Device-to-Device Error: ±5%; Channel-to-Channel Error: ±5%
  Ultralow Quiescent Current
  Shutdown Mode: 1uA (Max.) when EN = LOW
  Power Saving Mode: 10uA (Typ.) when EN = HIGH & All LEDs Off > 30ms
  Integrated 12 Bit, 29 kHz PWM Generator for each channel
  Independent Color Mixing Register per channel
  Independent Brightness Control Register per RGB LED Module
  Optional Logarithmic- or Linear-Scale Brightness Control
  Integrated 3-Phase-Shifting PWM Scheme
  3 Programmable Banks (R/G/B) for Easy Software Control of each Color
Two External Hardware Address Pins for Connection up to 4 Devices
Broadcast Slave Address for Configuring Multiple Devices Simultaneously
Auto-Increment Writing or Reading Consecutive Registers within one Transmission
Up to 400K Hz Fast-Mode I2C Speed
Features
Benefits
Smart Speaker, Smart Home Appliance
Doorbell, Electric Lock
Smoke Detector, Thermostat
Set-Top Box, Smart Router
Bluetooth® Headset, Handheld Device
Applications
Easy and Optimized Design for Color Mixing and Brightness Smooth Control with high resolution PWM generators in each channel
29KHz internal PWM Generators offer enough margin to eliminate the audible noise
Easy Software Control of Each Color and Good Channels Synchronization with 3 programmable banks
Balance System Level Power Consumption without Side Effect for LED Animation by ultralow quiescent current in Power Save Mode
Minimize the Input Power Budget with 3 phases PWM shifting
LP50xx
36/30/24/18/12/9-Ch 12-Bit PWM Ultra-low Quiescent Current I2C RGB LED Drivers

## Slide 56: LP5036-Q1 36-Ch I2C RGB LED Driver
Operating Voltage Range:
  Vcc Range: 2.7V to 5.5V
  EN, SDA and SCL pins compatible with 1.8V, 3.3V and 5V Power rails
  Output Maximum Voltage: 6V
Constant Current Sinks with High Precision
  25.5 mA Maximum per Channel when VCC in full range.
  35 mA Maximum per Channel when VCC ≥ 3.3V.
  Device-to-Device Error: ±5%; Channel-to-Channel Error: ±5%
  Ultralow Quiescent Current
  Shutdown Mode: 1uA (Max.) when EN = LOW
  Power Saving Mode: 10uA (Typ.) when EN = HIGH & All LEDs Off > 30ms
  Integrated 12 Bit, 29 kHz PWM Generator for each channel
  Independent Color Mixing Register per channel
  Independent Brightness Control Register per RGB LED Module
  Optional Logarithmic- or Linear-Scale Brightness Control
  Integrated 3-Phase-Shifting PWM Scheme
  3 Programmable Banks (R/G/B) for Easy Software Control of each Color
Two External Hardware Address Pins for Connection up to 4 Devices
Broadcast Slave Address for Configuring Multiple Devices Simultaneously
Auto-Increment Writing or Reading Consecutive Registers within one Transmission
Up to 400K Hz Fast-Mode I2C Speed
Features
Benefits
Smart Speaker, Smart Home Appliance
Doorbell, Electric Lock
Smoke Detector, Thermostat
Set-Top Box, Smart Router
Bluetooth® Headset, Handheld Device
Applications
Easy and Optimized Design for Color Mixing and Brightness Smooth Control with high resolution PWM generators in each channel
26KHz internal PWM Generators offer enough margin to eliminate the audible noise
Easy Software Control of Each Color and Good Channels Synchronization with 3 programmable banks
Balance System Level Power Consumption without Side Effect for LED Animation by ultralow quiescent current in Power Save Mode
Minimize the Input Power Budget with 3 phases PWM shifting
56

## Slide 57
Adaptive charge pump with 1x and 1.5x gain provides up to 95% LED drive efficiency
200 nA typical shutdown current
Independently programmable constant current outputs with 8-bit current setting and 8-bit PWM control
Three program execution engines with flexible instruction set
Package: MicroSMD-20 package, 0.4 mm pitch
Blood Glucose Meter
Handheld POS Terminals
Electronic Access Control
Fun / Indicator lights
LCD sub-display backlighting
Keypad RGB backlighting
Where RGB Indication is needed
Features
Benefits
Applications
Inductorless high efficiency LED driver solution
Ultra low power consumption
Lighting engines allow autonomous pattern generation without processor
3 output supports 1x RGB LED for color lighting effects – Ability to generate wide range of colors
Small solution size
LP5521
3-Channel RGB, White-LED Driver With Internal Program Memory and Integrated Charge Pump

## Slide 58
  Flexible control of LED lighting patterns
  Lots of current control for LED lighting and/or color balancing
  Full functionality over battery voltage range, down to 2.7V
  No need for extra memory chip or microcontroller
  Allows for GPIO triggering, rather than I2C write
  Low system power impact when disabled
Applications
E-cigarette
Smart phones
Tablets
Performance Displays
Conference phones
LCD sub-display backlighting
Keypad RGB backlighting and phone cosmetics
Vibra, speakers, waveform generator
Features
Benefits
Three independent engines
25.5mA full scale, 8 bit current resolution, 12 bit PWM control
Adaptive high efficiency charge pump
Internal program memory
Trigger input interface
20nA typical standby current
24 pin 2.3mm x 2.3mm DSBGA-26 package
LP5523
9-Channel RGB-, White-LED Driver With Internal Program Memory and Integrated Charge Pump

## Slide 59
I2C Interface Common Anode LED Drivers
4 CHs Constant Current Range: 0 – 25.5mA
8-Bit Individual Dot Correction
8-Bit Individual PWM Dimming
Output Current Error: +-5%, Channel to Channel Error: +-2%
Autonomous Operation With Program Execution Engines
    SRAM Memory for Sequences
    LOOPs, RAMPs, TRIGGERs, INT
Ultra Low Power Operation
    Standby supply current (EN = 0, CHIP_EN = 0): 200nA
    Automatic Power-Save Mode With External Clock: 10uA
    Package: DSBGA (12), 1.648 mm × 1.248 mm
  RGB LED support with extra message indicator or 4 channel keyboard backlight support
  Flexible lighting effects and run times for system efficiency savings and autonomous operation
  Low power
  System power savings when in shutdown or active
Applications
Fun Lights
Indicator Lights
Keypad RGB Backlighting and Phone Cosmetics
Routers and Switches
Smart watches
Features
Benefits
LP5562
4-Ch RGB-,White-LED Driver With Internal Program Memory and Independent Channel Control

## Slide 60
Supply Voltage Range: 2.5-5.5V
9 High-Accuracy Current Sinks
  25.5 mA Maximum per Channel
  8-Bit Individual Current Control
  12-Bit 20-kHz Internal Individual PWM Control Without Audio Noise
Three Programmable LED Engines
  Independent Illumination Control Without Active Microcontroller Control
  Synchronization Among Multiple Devices
  Up to 256 Instructions in SRAM for Storing Lighting Patterns
  LP5523- and LP55231-Device-Compatible Command Set
  Flexible Dimming Control
  I2C Dimming Control
  Engine Dimming Control
  PWM Direct Input Dimming (100-Hz to 20-kHz)
Adaptive Charge-Pump to Drive High-VF LEDs With Low Battery Voltage
Master Fader Control Allows Dimming of Multiple LEDs by Writing to Only One Register to Reduce the I2C Bus Traffic
2-μA Low Standby Current and 10-μA in Automatic Power-Save Mode When LEDs Are Inactive
Package: WQFN-24, 4.00 mm × 4.00 mm
Features
Benefits
Smart Speaker, Smart Home Appliance
Doorbell, Electric Lock
Smoke Detector, Thermostat
Set-Top Box, Smart Router
Bluetooth® Headset, Handheld Device
Applications
Ultra smooth color changing and fading with high PWM resolution and dot correction
Autonomous operation reduces system power consumption when the processor in sleep mode
Easy coding for Flexible LED lighting Patterns
Full functionality over battery voltage range
Easy manufacturability with integrated diagnostic
60
PART NUMBER | GROUP | I2C SLAVE ADDRESS
LP5569RTWR | 0 | 32h-35h and 40h (40h is broadcast address)
LP5569ARTWR | 1 | 42h-45h and 40h (40h is broadcast address)
LP5569
9-Channel I2C RGB LED Driver With Engine Control and Charge Pump

## Slide 61
Audio synchronization for a single fun light LED
4 PWM controlled RGB LED drivers
High efficiency Boost DC-DC converter
SPI/I2C compatible interface
2 addresses in I2C compatible interface
LED connectivity test through the serial interface
Small 36-bump Micro SMD (3 mm x 3 mm x 0.6 mm) or 36-bump Micro SMDxt package (3 mm x 3 mm x 0.65 mm)
Cellular Phones
PDAs, MP3 players
Electronic smart locks
E-cigarettes
Features
Benefits
Applications
Integrated boost LED drive solution
Ultra low power consumption
Small solution size
LP55281
12-Channel RGB/White-LED Drive With Boost

## Slide 62
8/16 CHs Constant Current Range: 5mA to 120mA
Input Voltage Range: 3V to 5.5V
Maximum Output Voltage: 17V
Output Current Error: +-8%, Channel to Channel Error: +-6%
Global brightness control and Adjusted Through an External Resistor
Individual / Global 8 bits PWM Dimming
  256-Step Individual Dimming with 97KHz PWM Signal
  256-Step Group Dimming with 190Hz PWM Signal
  256-Step Group Blinking with Programmable Frequency
LED Open and Over temperature Detection
4 Hardware Address Pins Allow 14 Devices
1MHz Fast-Mode Plus / 400KHz Fast-Mode / 100KHz Standard I2C Speed
25-MHz Internal Oscillator Requires No External Components
Packages: TSSOP VQFN
  TLC59108: TSSOP-20, VQFN-20
  TLC59116: TSSOP-28, VQFN-32
Applications
Features
Gaming
Small Signage
Industrial Equipment
Flexible LED connection
High current capacity
FM+ Transfer Rate Support
Accurate constant current driving
Comfortable user control
Benefits
TLC59108 / 116
8-CH/16-CH I2C Bus Constant-Current LED Drivers